## Slide 1: Chapter 1: Introduction to the Personal Computer
IT Essentials v6.0
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 1: Introduction to the Personal Computer

## Slide 2: Chapter 1 - Sections & Objectives
1.1 Personal Computer Systems
  Explain how personal computer systems work together
1.2 Select Computer Components
  Select appropriate computer components
1.3 Configurations for Specialized Computer Systems
    Explain how hardware is configured for task-specific computers
Notes: 2

## Slide 3: 1.1 Personal Computer Systems
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 1: Introduction to the Personal Computer

## Slide 4: Personal Computer Systems Cases and Power Supplies
Cases
  Influences the motherboard form factor choice
  Must allow for good air flow
  Available in different sizes
Power Supplies
  Provides power to all computer components.
  Must be chosen based on current and future needs.
  Deliver different voltage levels to meet different internal component needs.
Power Supply Wattage
  P = V x A
Notes: 1.1 - Personal Computer Systems
1.1.1 - Cases and Power Supplies

## Slide 5: Personal Computer Systems Internal PC Components
Motherboards
  Backbone of the computer
  Interconnects computer components
CPU
  The brain of the computer
  Most processing is done by the CPU
Cooling Systems
  Dissipates the heat generated by computer components.
Memory (ROM and RAM)
  RAM: Stores data temporarily, aiding processing
  ROM: Stores data permanently; often storing firmware and low level programs.
Notes: 1.1 - Personal Computer Systems
1.1.2 - Internal PC Components

## Slide 6: Personal Computer Systems Internal PC Components (Cont.)
Adapter Cards and Expansion Slots
  Adapter Cards extend computer functionality
  Adapter Cards connect to the motherboard through Expansion Slots
Storage Devices
  Designed to permanently store user data, user applications and the Operating System
  Can be internal or external to the computer
Video Ports
  Connects a video system to an external display device such as a monitor or projector
  Video systems are often designed as an adapter card.
General Ports
  Provide connectivity between the motherboard and various external devices such as printers, external storage and video cameras.
Notes: 1.1 - Personal Computer Systems
1.1.2 - Internal PC Components (Cont.)

## Slide 7: Personal Computer Systems External Ports and Cables
Video Ports and Related Cables
  A few different standards govern video traffic between the computer and external video devices.
  HDMI and displayPort are examples of video ports that require a specific cable to operate.
Other Ports and Related Cables
  Motherboards have a number of other ports used for device connectivity; USB is a common example.
Adapters and Converters
  Adapters and converters can be a solution if a motherboard does not have the proper port to connect to a device.
  Adapters do not usually process the signal; they simply redirect it to another pin.
  Converters are more likely to process and transform the signal, converting it to be accepted by an existing port.
Notes: 1.1 - Personal Computer Systems
1.1.3 - External Ports and Cables

## Slide 8: 1.2 Select Computer Components
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 1: Introduction to the Personal Computer

## Slide 9: Select Computer Components Select PC Components
Select the Motherboard, CPU, Case and Memory
  CPU, memory, motherboard and case choices are inter-related.
  The motherboard should support all customer required applications and still fit properly in the case.
  The case should host the motherboard, the proper power supply and provide good airflow for the internal components.
  The CPU must be compatible with motherboard CPU slot and voltage; it should be compatible with the chosen memory speed for maximum performance.
  The memory must also be compatible with motherboard memory slots and voltage.
  The amount of memory will depend on the type of applications requested by the customer.
Notes: 1.2 - Select Computer Components
1.2.1 - Select PC Components

## Slide 10: Select Computer Components Select PC Components (Cont.)
Select the Case and Fans
  Case and fans must be chosen to maximize internal airflow.
  The fans must fit the case and be within the power limits provided by the power supply.
Select the Power Supply
  The power supply should be selected based on the maximum amount of power required by all the internal components.
  Remember that some components will draw more power while under heavy load.
Select Adapter Cards
  Make sure the motherboard has compatible expansion slots to support the adapter cards.
  The motherboard must also have enough expansion slots to receive all the required adapter cards.
  Customer needs will define what adapter cards must be procured and installed.
Notes: 1.2 - Select Computer Components
1.2.1 - Select PC Components (Cont.)

## Slide 11: Select Computer Components Select PC Components (Cont.)
Select Hard Drives
  Important hard drive factors to be considered are speed, storage space and communication interface type.
  The drive’s underlying technology (HDD vs SSD) directly impacts speed.
Select a Media Reader
  The media reader must be compatible with customer media.
Select Optical Drives
  Make sure the drive is compatible with customer media.
  Other factors to consider are speed, communication interface type and the ability to write to the media.
Notes: 1.2 - Select Computer Components
1.2.1 - Select PC Components (Cont.)

## Slide 12: Select Computer Components Select PC Components (Cont.)
Select External Storage
  Important factors when selecting external storage are storage space, speed and communication interface.
  Make sure the computer has enough ports to accommodate the external devices and peripherals.
  Note: Some external devices do not require an external power supply but rely on a second USB port for power.
Select I/O Devices
  The selection of I/O devices is application specific and will depend on customer requirements.
  Make sure the computer has enough communication ports and that they are compatible with the types required by the I/O devices.
Notes: 1.2 - Select Computer Components
1.2.1 - Select PC Components (Cont.)

## Slide 13: 1.3 Configurations for Specialized Computer Systems
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 1: Introduction to the Personal Computer

## Slide 14: Configurations for Specialized Computer Systems Specialized Computer Systems
Thick and Thin Clients
  Thin clients have little processing power and are designed to act as a terminal to a server (thick client).
  Thick clients have more powerful CPUs, more memory and their own storage. They serve as processing stations for thin clients.
CAx Workstations
  Designed to support CAD and CAM applications.
  Plenty of RAM, fast disks, powerful CPU and special input devices are common resources.
Audio and Video Editing Workstations
  Common editing workstation resources include much RAM, fast disks, powerful CPU and special adapter cards such as audio and video capture.
Notes: 1.3 - Configurations for Specialized Computer Systems
1.3.1 - Specialized Computer Systems

## Slide 15: Configurations for Specialized Computer Systems Specialized Computer Systems (Cont.)
Virtualization Workstations
  These workstations are designed to run virtual computers
  Virtual computers use and share the workstation’s physical resources such as CPU, memory and disks.
  The selection of physical resources will depend on the number and purpose of the virtual machines.
Gaming PCs
  Due to high resource requirements of modern games, gaming PCs are very resource demanding.
  A few requirements of gaming PCs are: top end CPU, lots of fast RAM, fast disks, high performance input devices and audio systems.
Home Theatre PCs
  These computers must be able to play various media formats and, in some cases, receive TV signals.
  Common HTPC requirements include powerful CPU, fast RAM, large disks, fast NIC and video card with TV input.
Notes: 1.3 - Configurations for Specialized Computer Systems
1.3.1 - Specialized Computer Systems (Cont.)

## Slide 16: 1.4 Chapter Summary
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 1: Introduction to the Personal Computer

## Slide 17: Chapter Summary Summary
This chapter introduced the components that comprise a personal computer system and what to consider when choosing upgrade components.
Information technology encompasses the use of computers, network hardware, and software to process, store, transmit, and retrieve information.
A personal computer system consists of hardware components and software applications.
The computer case and power supply must be chosen carefully to support the hardware inside the case and allow for the addition of components.
The internal components of a computer are selected for specific features and functions. All internal components must be compatible with the motherboard.
Use the correct type of ports and cables when connecting devices.
Typical input devices include the keyboard, mouse, touch screen, and digital cameras.
Typical output devices include monitors, printers, and speakers.
Cases, power supplies, the CPU and cooling system, RAM, hard drives, and adapter cards, must be upgraded when devices fail or no longer meet customer needs.
Specialized computers require hardware specific to operate. The type of hardware used in specialized computers is determined by how a customer works and what a customer wants to accomplish.
Notes: 1.4.1.1 - Summary

## Slide 19: Assignment 1 –PC Component Research
Choose 10 terms from the slideshow that you have heard of but maybe do not fully understand.
Search for more information on these terms and record a definition in your own words.
The final product can be a word doc or PowerPoint and will be uploaded to Moodle.

## Slide 20: Section 1.1 New Terms and Commands
adapter
agp
amd
amplifier
analog
architecture
ata
atx
atx12v
backbone
biometric
bios
bit
bnc
bus
byte
cache
capacitors
card
cartridge
case
cathode
chassis
chip
chipset
cisc
coaxial
computer
cooling
cpu
crt
desktop
digital
digitizer
diode
dip
disk
display
displayport
Notes: New Terms and Commands

## Slide 21: Section 1.1 New Terms and Commands (cont.)
dlp
dot pitch
drive
dvd
dvi
eisa
eps12v
ethernet
eufi
fan
firmware
flash
floppy
fps
fsb
gamepads
ghz
gui
hardware
hdd
hdmi
headphones
heatsink
hertz
hub
intel
gpu
grounded
keyboard
kvm
laptop
lasers
lcd
led
lga
mca
mhz
microchannel
micromirror
Notes: New Terms and Commands (cont.)

## Slide 22: Section 1.1 New Terms and Commands (cont.)
microphone
microprocessor
midi
mobile
modem
monitor
monochromatic
motherboard
multicore
nic
nonvolatile
northbridge
ohms
oled
optical
outlets
overclocking
pathways
pcb
pci
pga
pixel
plasma
power
printers
processor
program
qsxga
radiator
radio
ram
rca
resistance
resolution
rgb
risc
rom
rpm
sata
Notes: New Terms and Commands (cont.)

## Slide 23: Section 1.1 New Terms and Commands (cont.)
satellite
scanner
screen
scsi
semiconductor
serial
servers
setup
signal
sink
slot
software
southbridge
speakers
spindle
sram
ssd
ssds
sshd
storage
svga
swappable
switch
tape
terabytes
tft
thunderbolt
transistor
xga
uefi
uid
urls
usb
uxga
vga
volt
Voltage
wattage
watts
Notes: New Terms and Commands (cont.)

## Slide 24: Section 1.1 New Terms and Commands (cont.)
web
webcams
wireless
Notes: New Terms and Commands (cont.)